### Riech-O-Mat serial port communication to open/close valves
Channel 1 : airflow valve. Channels 2-5: odorant channels.
Baud rate 9600bps, 8 data bits, one stop bit, no parity. Each data frame contains eight bytes.
8 channel uart relay command.

Control command format:
Bytes Number	1	2	3	4	5	6	7	8
	Frame head		Reserved bytes			Channel	Command	checksum
Reading status	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	00	0xAB / 0xAC / 0xAD / 0xAE / 0xAF / 0xB0 / 0xB1 / 0xB2
Relay open	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	01	0xAD / 0xAE / 0xAF / 0xB0 / 0xB1 / 0xB2 / 0xB3 / 0xB4
Relay close	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	02	0xAE / 0xAF / 0xB0 / 0xB1 / 0xB2 / 0xB3 / 0xB4 / 0xB5
Relay toggle	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	03	0xAF / 0xB0 / 0xB1 / 0xB2 / 0xB3 / 0xB4 / 0xB5 / 0xB6
Relay momentary	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	04	0xB0 / 0xB1 / 0xB2 / 0xB3 / 0xB4 / 0xB5 / 0xB6 / 0xB7
Relay / Interlock	0x5556		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	05	0xB1 / 0xB2 / 0xB3 / 0xB4 / 0xB5 / 0xB6 / 0xB7 / 0xB8

5 Control commands：

1. Reading status（reading the satus of the relay (on/off)）

Channel 1 ：55 56 00 00 00 01 00 AC
Channel 2 ：55 56 00 00 00 02 00 AD
Channel 3 ：55 56 00 00 00 03 00 AE
Channel 4 ：55 56 00 00 00 04 00 AF
Channel 5 ：55 56 00 00 00 05 00 B0
Channel 6 ：55 56 00 00 00 06 00 B1
Channel 7 ：55 56 00 00 00 07 00 B2
Channel 8 ：55 56 00 00 00 08 00 B3

2. Relay open (issue this command ，Relay open , COM connect to NO ）

Channel 1 ：55 56 00 00 00 01 01 AD
Channel 2 ：55 56 00 00 00 02 01 AE
Channel 3 ：55 56 00 00 00 03 01 AF
Channel 4 ：55 56 00 00 00 04 01 B0
Channel 5 ：55 56 00 00 00 05 01 B1
Channel 6 ：55 56 00 00 00 06 01 B2
Channel 7 ：55 56 00 00 00 07 01 B3
Channel 8 ：55 56 00 00 00 08 01 B4

3. Relay close (issue this command ，Relay close , COM disconnect NO , and COM connect to NC ）

Channel 1 ：55 56 00 00 00 01 02 AE
Channel 2 ：55 56 00 00 00 02 02 AF
Channel 3 ：55 56 00 00 00 03 02 B0
Channel 4 ：55 56 00 00 00 04 02 B1
Channel 5 ：55 56 00 00 00 05 02 B2
Channel 6 ：55 56 00 00 00 06 02 B3
Channel 7 ：55 56 00 00 00 07 02 B4
Channel 8 ：55 56 00 00 00 08 02 B5

4. Relay toggle（Relay status reversal，if COM connect to NO，this commands will Disconnect COM to NO and Reverse COM connect to NC，and vice versa）

Channel 1 ：55 56 00 00 00 01 03 AF
Channel 2 ：55 56 00 00 00 02 03 B0
Channel 3 ：55 56 00 00 00 03 03 B1
Channel 4 ：55 56 00 00 00 04 03 B2
Channel 5 ：55 56 00 00 00 05 03 B3
Channel 6 ：55 56 00 00 00 06 03 B4
Channel 7 ：55 56 00 00 00 07 03 B5
Channel 8 ：55 56 00 00 00 08 03 B6

5. Relay momentary（Relay COM connect to NO，disconnect after 200MS ）

Channel 1 ：55 56 00 00 00 01 04 B0
Channel 2 ：55 56 00 00 00 02 04 B1
Channel 3 ：55 56 00 00 00 03 04 B2
Channel 4 ：55 56 00 00 00 04 04 B3
Channel 5 ：55 56 00 00 00 05 04 B4
Channel 6 ：55 56 00 00 00 06 04 B5
Channel 7 ：55 56 00 00 00 07 04 B6
Channel 8 ：55 56 00 00 00 08 04 B7

6. Relay Interlock

Channel 1 ：55 56 00 00 00 01 05 B1
Channel 2 ：55 56 00 00 00 02 05 B2
Channel 3 ：55 56 00 00 00 03 05 B3
Channel 4 ：55 56 00 00 00 04 05 B4
Channel 5 ：55 56 00 00 00 05 05 B5
Channel 6 ：55 56 00 00 00 06 05 B6
Channel 7 ：55 56 00 00 00 07 05 B7
Channel 8 ：55 56 00 00 00 08 05 B8

Once issue a command, will have a return fame , 7th byte of return fame mean the satus of realy .

Return command format:

Bytes Number	1	2	3	4	5	6	7	8
	Frame head		Reserved bytes			Channel	Command	checksum
Return relay open	0x333C		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	01	0x71 / 0x72 / 0x73 / 0x74 / 0x75 / 0x76 / 0x77 / 0x78
Return relay close	0x333C		0x000000			0x01 Channel 1 / 0x02 Channel 2 / 0x03 Channel 3 / 0x04 Channel 4 / 0x05 Channel 5 / 0x06 Channel 6 / 0x07 Channel 7 / 0x08 Channel 8	02	0x72 / 0x73 / 0x74 / 0x75 / 0x76 / 0x77 / 0x78 / 0x79

2 return command

1、Return relay open（return this command，mean COM connect to NO ）

Channel 1 ：33 3C 00 00 00 01 01 71
Channel 2 ：33 3C 00 00 00 02 01 72
Channel 3 ：33 3C 00 00 00 03 01 73
Channel 4 ：33 3C 00 00 00 04 01 74
Channel 5 ：33 3C 00 00 00 05 01 75
Channel 6 ：33 3C 00 00 00 06 01 76
Channel 7 ：33 3C 00 00 00 07 01 77
Channel 8 ：33 3C 00 00 00 08 01 78

2、Return relay close（return this command，mean COM disconnect NO , and COM connect to NC ）

Channel 1 ：33 3C 00 00 00 01 02 72
Channel 2 ：33 3C 00 00 00 02 02 73
Channel 3 ：33 3C 00 00 00 03 02 74
Channel 4 ：33 3C 00 00 00 04 02 75
Channel 5 ：33 3C 00 00 00 05 02 76
Channel 6 ：33 3C 00 00 00 06 02 77
Channel 7 ：33 3C 00 00 00 07 02 78
Channel 8 ：33 3C 00 00 00 08 02 79